China 400 Series Planetary Gear box, Manufacturer, Supplier, Factory, Exporter in china

|  | 400 Series Planetary Drives Planetary Gear Model 400 Series Ratio 5-28 Output Torque 1000-180000N.m 400 series hydraulic transmission can endure the large outside radial and axial forces. It features for high torque, high starting efficiency, low speed stability and low noisy operating.Thus it is widely used in construction machinery, railway, ship, petroleum, mining and metallurgy equipments. Features: One-or two-stage planetary gearboxes, smooth operation and reasonable structure.Small volume, compact structure and high transmission efficiency.Radial piston hydraulic motor with long life operating.Mounting dimension is available on request.Brake, balance valve, shuttle valve and the distributor which can integrate all kinds of function valve are also available on request. Model Ratio (i) Output Torque (Nm) Speed 400-2.5 2.5, 5 2976 0-100 400-1C3 5 4361 0-90 400-3 5, 5.5 6492 0-90 400-4 5, 5.5 13538 0-80 400-5 5, 5.5 31159 0-70 400-6 5, 5.5 57141 0-40 400-7 5, 5.5 68092 0-35 400-2.53 20 9856 0-19 400-34 20, 28 18725 0-18 400-45 20, 28 32682 0-15 400-56 20, 28 63078 0-14 400-67 20, 28 100136 0-13 400-79 20, 28 187290 0-9 download: |
| --- | --- |

Hydraulic Motor,Radial Piston Hydraulic Motor,Hydraulic Orbital Motor,MS Series Hydraulic Motor,Axial piston hydraulic motor,Hydraulic Winch,Hoisting Winch,Free Fall Hydraulic Winch,Recovery Winch,Planetary Gearbox,300 Series Planetary Gearboxes,In-Line Planetary Gearbox,Right-Angle Planetary Gearbox,foot mounted planetary gearbox,400 Series Planetary Gear box,Final Drive,GFT Series Travel Drive,TGM Series Excavator Final Drive,Slew Drive,Wheel Drive,Winch Drive,Track Undercarriage,Steel Tracked Undercarriage,Rubber Tracked Undercarriage,Hydraulic Pump,

NINGBO BONNY HYDRAULICS TRANSMISSION CO.,LTD Add: No.36, the third road of Dagang, Beilun,Ningbo, Zhejiang, China Contact: Cathy Hsu (Sales Manager) Tel: +86-574-86879210 Fax: +86-574-86877981 E-mail:sales@bonnyhydraulic.com WebSite: http://www.bonnyhydraulic.com