China Axial piston hydraulic motor, Manufacturer, Supplier, Factory, Exporter in china

|  | A6V Series Bent Axis Hydraulic Motor Rexroth Hydraulic Motor Model A6VE Series Replace for Rexroth A6VE Series hydraulic motor Displacement 107cc - 250cc/rev The hydraulic motor A6VE, axial tapered piston bent-axis design, suitable for hydrostatic drives in open and closed circuits. It is widely applied in mobile and industrial applications .Output speed depends on the flow capacity of the pump and the displacement of the motor. The torque increase with the pressure differential between the high and low pressure side and with increasing displacement. And it can be completely interchanged with Rexroth A6VE series hydraulic motor. Features: 1. Plug-in motor, preferably for installation in mechanical gearboxes 2. Wide control range (can be swiveled over zero), high speeds and high torque 3. Option: Integrated or built-on flushing and boost pressure valves 4. Counterbalance valve integrated into the port plate (A6VE), sizes 107 - 250 5. Totally interchangeable with original Rexroth A6VE series Hydraulic Motor Size A6VE 107 160 250 Swept volume Vg max cm3 107 160 250 Swept volume Vg,1 cm3 68 101 190 Speed 1) at Vg max nmax rpm 3550 3100 2700 at Vg < Vg,1 nmax rpm 5600 4900 3600 Flow at nmax qVmax l/min 380 496 675 Torque p = 350 bar Tmax Nm - - 1391 p = 400 bar Tmax Nm 681 1019 - Weight (approx.) m kg 47 64 90 1)0 Maintaining qV max |
| --- | --- |
|  | A6V Series piston motor Model A6V Series Replace for Rexroth A6Vm Series hydraulic motor Displacement 28cc - 1000cc/rev This series of bent axial piston hydraulic motor has a compact and small volume,low weight,high pressure,widely speed and high starting efficiency. It is widely applied in engineering machine,crane and transport machine,shipping,mining,metallurgy,machine tool etc. Features 1. Adopt axial piston oil distributing, compact volume, high pressure and speed. 2. Using sphere oil distributing, High volume and working efficiency. 3. Adjustable displacement, enhancing the output speed at small angle. 4. Reversible rotating orientation, radial and axial load available. 5. Can be using as a pump in some close system. 6. Complete interchange with Rexroth A6VM series bent axial piston hydraulic motor on performance and dimensions. Size A6VM 28 55 80 107 140 160 200 250 355 500 1000 Swept volume Vg max cm3 28,1 54,8 80 107 140 160 200 250 355 500 1000 Swept volume Vg,1 cm3 18 35 51 68 88 101 126 190 270 385 762 Speed at Vg max nmax rpm 5550 4450 3900 3550 3250 3100 2900 2700 2240 2000 1600 at Vg < Vg,1 nmax rpm 8750 7000 6150 5600 5150 4900 4600 3600 2950 2650 2100 Flow at nmax qVmax l/min 156 244 312 380 455 496 580 675 795 1000 1600 Torque p = 350 bar Tmax Nm - - - - - - - 1391 1978 2785 5571 p = 400 bar Tmax Nm 179 349 509 681 891 1019 1273 - - - - |
|  | Replace Rexroth A2FE Series Hydraulic Motor Model A2FE Series Replace for Rexroth A2FE Series hydraulic motor Displacement 28cc - 355cc/rev Speed 0-6300rpm Bonny Hydraulics is supplying several kinds of replacement hydraulic axial piston pumps or motors for Rexroth, Vickers and Kawasaki. All of these motors are completely news on casting housing and spare parts inside. However, we do very strict tests in our company before shipment. So these motors are not only the same on dimensions of original hydraulic motor, but also are the same performance with original ones. Features: 1. Counterbalance valve can be fitted 2. Option: Integrated pressure relief valve 3. Option: Integrated or built-on flushing and boost pressure valves 4. Suitable for use as pump in closed circuits 5. Long-life bearings available (sizes 250 - 355) 6. Totally interchangeable with original Rexroth A2FE series Hydraulic Motor Size A2FE 28 32 45 56 63 80 90 107 125 Swept volume Vg cm3 28,1 32 45,6 56,1 63 80,4 90 106,7 125 Speed 1) nmax rpm 6300 6300 5600 5000 5000 4500 4500 4000 4000 Flow at nmax qVmax l/min 176 201 255 280 315 360 405 427 500 Torque p=400bar Tmax Nm 178 204 290 356 400 508 572 680 796 Weight (approx.) m kg 9,5 9,5 13,5 18 18 23 23 32 32 Size A2FE 160 180 250 355 Swept volume Vg cm3 160,4 180 250 355 Speed 1) nmax rpm 3600 3600 2700 2240 Flow at nmax qVmax l/min 577 648 675 795 Torque p=350bar Tmax Nm - - 1393 1978 p=400bar Tmax Nm 1016 1144 - - Weight (approx.) m kg 45 45 73 110 |
|  | Replace Rexroth A2FM Series Hydraulic Motor Model A2FM Series Replace for Rexroth A2FM Series hydraulic motor Displacement 5cc - 1000cc/rev Speed 0 - 10000rpm This fixed axial displacement piston motor A2FM, bent axis design, suitable for hydrostatic drives in open and closed circuits. It is widely applied in mobile and industrial applications .Output speed depends on the flow capacity of the pump and the displacement of the motor. The torque increase with the pressure differential between the high and low pressure side and with increasing displacement. And it can be completely interchanged with Rexroth A2FM series hydraulic motor. Features: 1. Counterbalance valve can be fitted 2. Option: Integrated pressure relief valve 3. Option: Integrated or built - on flushing and boost pressure valves 4. Suitable for use as pump in closed circuits 5. Long - life bearings available (sizes 250 - 1000) 6. Totally interchangeable with original Rexroth A2FM series Hydraulic Motor Size A2FM 5 10 12 16 23 28 32 45 56 63 80 Swept volume Vg cm3 4,93 10,3 12 16 22,9 28,1 32 45,6 56,1 63 80,4 Speed 1) nmax rpm 10000 8000 8000 8000 6300 6300 6300 5600 5000 5000 4500 Flow at nmax qVmax l/min 49 82 96 128 144 176 201 255 280 315 360 Torque p=315bar Tmax Nm 24,7 - - - - - - - - - - p=400bar Tmax Nm - 65 76 100 144 178 204 290 356 400 508 Weight (approx.) m kg 2,5 5,4 5,4 5,4 9,5 9,5 9,5 13,5 18 18 23 Size A2FM 90 107 125 160 180 200 250 355 500 710 1000 Swept volume Vg cm3 90 106,7 125 160,4 180 200 250 355 500 710 1000 Speed 1) nmax rpm 4500 4000 4000 3600 3600 2750 2700 2240 2000 1600 1600 Flow at nmax qVmax l/min 405 427 500 577 648 550 675 795 1000 1136 1600 Torque p=350bar Tmax Nm - - - - - - 1393 1978 2785 3955 5570 p=400bar Tmax Nm 572 680 796 1016 1144 1272 - - - - - Weight (approx.) m kg 23 32 32 45 45 66 73 110 155 325 336 |

Hydraulic Motor,Radial Piston Hydraulic Motor,Hydraulic Orbital Motor,MS Series Hydraulic Motor,Axial piston hydraulic motor,Hydraulic Winch,Hoisting Winch,Free Fall Hydraulic Winch,Recovery Winch,Planetary Gearbox,300 Series Planetary Gearboxes,In-Line Planetary Gearbox,Right-Angle Planetary Gearbox,foot mounted planetary gearbox,400 Series Planetary Gear box,Final Drive,GFT Series Travel Drive,TGM Series Excavator Final Drive,Slew Drive,Wheel Drive,Winch Drive,Track Undercarriage,Steel Tracked Undercarriage,Rubber Tracked Undercarriage,Hydraulic Pump,

NINGBO BONNY HYDRAULICS TRANSMISSION CO.,LTD Add: No.36, the third road of Dagang, Beilun,Ningbo, Zhejiang, China Contact: Cathy Hsu (Sales Manager) Tel: +86-574-86879210 Fax: +86-574-86877981 E-mail:sales@bonnyhydraulic.com WebSite: http://www.bonnyhydraulic.com