China Hoisting Winch, Manufacturer, Supplier, Factory, Exporter in china

|  | AF Series Hydraulic Winch Model AF Series Pull Force 5700-45000kgs Rope Speed 0- 83m/min Application ship crane, harbor, petroleum, drill machine, engineering machinery, geological exploration and construction machinery Hydraulic WinchesAF series high-power hoisting winches are widely used in ship crane, harbor, petroleum, drill machine, engineering machinery, geological exploration and construction machinery. It is the best choice for those situations which requires large power, high speed and high security. Special Features: Two-or three-stage planetary gearboxes, smooth operation and reasonable structure. Normally closed friction type brake, high braking torque, safe and reliable operating. Small volume, compact structure and high transmission efficiency. Axial fixed or variable hydraulic motor with long life operating. Mounting frame is available on request. Balance valve, shuttle valve, limit switch and other accessories are also available on request. Model W.L.L.1st layer W.L.L.top layer Rope Speed Rope diam. Capacity of Rope Working Pressure Max Supply Oil Flow Download kgf kgf m/min mm m Mpa L/min PDF AF5700 5700 4500 60 16 107 25 160 AF7700 7700 6000 52 18 118 25 180 AF9600 9600 7500 43 20 118 25 180 AF12800 12800 9800 43 24 118 27 220 AF15000 15000 12800 39 24 110 25 220 AF18500 18500 14600 85.3 28 162 27 380 AF25000 25000 19500 48.1 30 162 27 380 AF30000 30000 23000 32 32 169 30 380 AF45000 45000 34700 32 42 169 30 380 |
| --- | --- |
|  | BG Series Hydraulic Winch crane winch BG Series Hydraulic Winch for crane, drilling rig machine, piling machine Model BG Series winch Pull Force 500 - 5700kgs Rope Speed 0- 63m/min Application Pick n carry crane, mobile crane, drill machine, piling machine. overhead working truck, lorry mounted crane, mirror crane, ship equipments and so on BG series hoisting winches are widely used in overhead working truck, lorry mounted crane, drill machine, mirror crane, ship equipments and so on. It is the best choice for those situations that requires the narrow space and light weight. Special Features Floating type planetary gearbox, smooth operation and reasonable structure. Normally closed friction type brake, high braking torque, safe and reliable operating. Small volume, compact structure and high transmission efficiency. Long life Danfoss hydraulic orbit motor Mounting frame is available on request. Balance valve, shuttle valve, limit switch and other accessories are also available on request. Model W.L.L.1st layer W.L.L.top layer Rope Speed Ropediam. Capacity of Rope Working Pressure Max Supply Oil Flow Download kgf kgf m/min mm m Mpa L/min PDF BG500 500 380 63 6 67 14 40 BG800 800 680 54 8 53 14 50 BG1100 1100 870 41 8 53 14 50 BG1300 1300 1000 45 9 48 14 55 BG1500 1500 1200 42 10 60 21 55 BG2000 2000 1600 35 10 60 21 55 BG2500 2500 2000 52 12 52 21 100 BG2600 2600 2000 54 12 76 21 100 BG3200 3200 2500 44 14 66 21 100 BG3600 3600 2800 40 14 66 21 100 BG4500 4500 3500 36 15 89 21 110 BG5700 5700 4500 26 16 102 21 120 |
|  | GH Series Hydraulic Winch Model GH Series Pull Force 1000 - 40000kgs Rope Speed 0- 40m/min Application marine deck machinery, harbor, petroleum, drill machine, mining, geological exploration and construction machinery GH series hydraulic winches are widely used in marine deck machinery, harbor, petroleum, drill machine, mining, geological exploration and construction machinery. Special Features One-or two-stage planetary gearboxes, smooth operation and reasonable structure. Normally closed friction type brake, high braking torque, safe and reliable operating. Small volume, compact structure and high transmission efficiency. Radial piston hydraulic motor with long life operating. Mounting frame is available on request. Balance valve, shuttle valve, limit switch and other accessories are also available on request. Model W.L.L.1st layer W.L.L.top layer Rope Speed Rope diam. Capacity of Rope Working Pressure Max Supply Oil Flow Download kgf kgf m/min mm m Mpa L/min GH1000 1000 860 25 10 60 15 25 GH2000 2000 1700 25 12 50 14 50 GH3000 3000 2500 35 15 65 16 95 GH4000 4000 3300 35 16 65 14 125 GH5000 5000 4200 40 20 87 14 175 GH6000 6000 4900 40 21.5 68 14 215 GH8000 8000 6700 40 24 100 14 270 GH10000 10000 7800 40 28 90 13 380 GH12000 12000 10000 30 30 176 17 270 GH15000 15000 12000 30 34 153 18 320 GH18000 18000 15000 30 38 143 18 375 GH20000 20000 16000 32 40 150 18 440 GH24000 24000 19000 32 42 140 17 480 GH25000 25000 20000 14 42 110 14 360 GH28000 28000 23000 14 44 105 14 380 GH30000 30000 25000 16 44 155 18 370 GH35000 35000 29000 16 46 150 18 390 GH40000 40000 33000 16 48 145 18 440 |
|  | GW Series Hydraulic Winch Model GW Series Pull Force 1000 - 18000kgs Rope Speed 0- 40m/min Application marine deck machinery, harbor, petroleum, drill machine, engineering machinery, mining, geological exploration and construction machinery. GW series hydraulic winches are widely used in marine deck machinery, harbor, petroleum, drill machine, engineering machinery, mining, geological exploration and construction machinery. Special Features One-or two-stage planetary gearboxes, smooth operation and reasonable structure. Normally closed friction type brake, high braking torque, safe and reliable operating. Small volume, compact structure and high transmission efficiency. Radial piston hydraulic motor with long life operating. Mounting frame is available on request. Balance valve, shuttle valve, limit switch and other accessories are also available on request. Model W.L.L.1st layer W.L.L.top layer Rope Speed Rope diam. Capacity of Rope Working Pressure Max Supply Oil Flow Download kgf kgf m/min mm m Mpa L/min GW1000 1000 860 30 10 60 16 40 GW2000 2000 1680 30 12 50 16 70 GW3000 3000 2526 35 15 65 16 80 GW4000 4000 3335 35 16 65 17 100 GW5000 5000 4167 40 20 87 16 160 GW6000 6000 4922 40 21.5 68 16 190 GW8000 8000 6698 40 24 100 16 260 GW10000 10000 7846 40 28 90 16 310 GW12000 12000 10080 30 30 175 17 270 GW15000 15000 9880 25 34 150 20 240 GW18000 18000 14700 30 38 143 18 360 |

Hydraulic Motor,Radial Piston Hydraulic Motor,Hydraulic Orbital Motor,MS Series Hydraulic Motor,Axial piston hydraulic motor,Hydraulic Winch,Hoisting Winch,Free Fall Hydraulic Winch,Recovery Winch,Planetary Gearbox,300 Series Planetary Gearboxes,In-Line Planetary Gearbox,Right-Angle Planetary Gearbox,foot mounted planetary gearbox,400 Series Planetary Gear box,Final Drive,GFT Series Travel Drive,TGM Series Excavator Final Drive,Slew Drive,Wheel Drive,Winch Drive,Track Undercarriage,Steel Tracked Undercarriage,Rubber Tracked Undercarriage,Hydraulic Pump,

NINGBO BONNY HYDRAULICS TRANSMISSION CO.,LTD Add: No.36, the third road of Dagang, Beilun,Ningbo, Zhejiang, China Contact: Cathy Hsu (Sales Manager) Tel: +86-574-86879210 Fax: +86-574-86877981 E-mail:sales@bonnyhydraulic.com WebSite: http://www.bonnyhydraulic.com