China In-Line Planetary Gearbox, Manufacturer, Supplier, Factory, Exporter in china

|  | In-Line Planetary Gears reducer gearbox Model In-Line Series Replace for Brevini ED, ET, EQ, EM, EC and EL series Bonfiglioli 300 series Dinamicoil RE, RA series Reggiane Riduttori RR series Ratio 3.4-5000 Output Torque 1000-450000N.m OverviewThe installation and overall dimension of planetary gearboxes are strictly designed in accordance with Italy and American manufacturers, so they can be completely interchangeable with Brevini ED, ET, EQ, EM, EC and EL series, Bonfiglioli 300 series and Dinamicoil RE, RA series on performance and connection dimensions. They are the ideal product to replace those Italian products. ConfigurationMounting solution: flange mounted, foot mounted, shaft mounted Features: Torque Range: 1000 ... 1.100.000 Nm Transmissible Mechanical Power: up to 450 kW Gear Ratios: i=3,4 ... 5.000 Gear Unit Versions Right angle (with a spiral bevel gear set) Output ConfigurationFoot and flange mounted Output shaft: solid with key, splined, splined hollow,hollow with shrink disc Input ConfigurationsFlanged axial piston hydraulic motorsHydraulic orbit motorsIEC and Nema motor adaptorsSolid input shaft Hydraulic BrakeHydraulically released parking brake on request Electric Brake: DC and AC type Size Rated Output Torque Max. Output Power Max. Input Speed Ratio Nm KW rpm i 200 1100 20 3000 3.4-2700 201 1700 30 3000 3.4-2700 240 2300 40 3000 3.6-2800 241 3700 50 3000 3.6-2500 280 5000 60 2500 3.6-2400 353 6000 72 2500 3.6-2400 354 8900 75 2000 4-2400 355 12500 90 2000 4-2400 428 15500 100 2000 4-2400 429 17000 110 2000 4-2400 445 19000 130 2000 4-2400 446 29000 155 2000 4-2100 542 36000 180 2000 4-2100 543 45000 200 1500 4.4-2000 695 82000 250 1500 4.4-1800 696 100000 270 1500 4.4-1200 download: |
| --- | --- |

Hydraulic Motor,Radial Piston Hydraulic Motor,Hydraulic Orbital Motor,MS Series Hydraulic Motor,Axial piston hydraulic motor,Hydraulic Winch,Hoisting Winch,Free Fall Hydraulic Winch,Recovery Winch,Planetary Gearbox,300 Series Planetary Gearboxes,In-Line Planetary Gearbox,Right-Angle Planetary Gearbox,foot mounted planetary gearbox,400 Series Planetary Gear box,Final Drive,GFT Series Travel Drive,TGM Series Excavator Final Drive,Slew Drive,Wheel Drive,Winch Drive,Track Undercarriage,Steel Tracked Undercarriage,Rubber Tracked Undercarriage,Hydraulic Pump,

NINGBO BONNY HYDRAULICS TRANSMISSION CO.,LTD Add: No.36, the third road of Dagang, Beilun,Ningbo, Zhejiang, China Contact: Cathy Hsu (Sales Manager) Tel: +86-574-86879210 Fax: +86-574-86877981 E-mail:sales@bonnyhydraulic.com WebSite: http://www.bonnyhydraulic.com