China MS Series Hydraulic Motor, Manufacturer, Supplier, Factory, Exporter in china

|  | Shaft Moutned MS series hydraulic motor Model MS Series Replace for Poclain MS Series, Bosh Rexroth MCR series Displacement 125-10000 ml/r Torque 394-45550 N.m MS series piston motor such characteristics as: high mechanical efficiency and high volumetric efficiency, thus it is widely used in the travelling movement of those wheel vehicle and mechanical hydraulic power system of engineering plant, agricultural machinery, coal mining machinery, lifting and transportation equipment, ship's deck machinery, geological prospecting equipments, etc. Features: Modular design and independent assortment on request Supporting axial and radial loading Double displacement output High working pressure, low speed stability and freewheel operation condition. The mounting dimension can be interchanged with Poclain MS, MSE and Bosh Rexroth MCR series. Model Displacement (ml/rpm) Rated pressure(MPa) Max pressure(MPa) Rated pitch of strand(N.m)(whole displacement) Speed range(rpm) Max power(kw)(whole displacement) Whole displacement Semi displacement MS02 213 25 40 796 0-310 16 MS05 468 234 25 40 1749 0-200 25 MS08 780 390 25 40 2914 0-170 36 MS11 1048 524 25 40 3916 0-160 44 MS18 1747 873 25 40 6528 0-150 62 MS25 2498 1249 25 40 9334 0-130 80 MS35 3494 1747 25 40 13055 0-100 97 MS50 4996 2498 25 40 18667 0-100 123 MS83 8328 4164 25 40 31098 0-80 176 download: |
| --- | --- |
|  | Wheel Mounted MS Series Wheel Motor Poclain Hydraulics Motor Model MS Series Replace for Poclain MS Series, Bosh Rexroth MCR series Displacement 125-10000 ml/r Torque 394-45550 N.m MS series piston motor such characteristics as: high mechanical efficiency and high volumetric efficiency, thus it is widely used in the travelling movement of those wheel vehicle and mechanical hydraulic power system of engineering plant, agricultural machinery, coal mining machinery, lifting and transportation equipment, ship's deck machinery, geological prospecting equipments, etc. Features:Modular design and independent assortment on request Supporting axial and radial loading Double displacement output High working pressure, low speed stability and freewheel operation condition. The mounting dimension can be interchanged with Poclain MS, MSE and Bosh Rexroth MCR series. Model Displacement (ml/rpm) Rated pressure(MPa) Max pressure(MPa) Rated pitch of strand(N.m)(whole displacement) Speed range(rpm) Max power(kw)(whole displacement) Whole displacement Semi displacement MS02 213 25 40 796 0-310 16 MS05 468 234 25 40 1749 0-200 25 MS08 780 390 25 40 2914 0-170 36 MS11 1048 524 25 40 3916 0-160 44 MS18 1747 873 25 40 6528 0-150 62 MS25 2498 1249 25 40 9334 0-130 80 MS35 3494 1747 25 40 13055 0-100 97 MS50 4996 2498 25 40 18667 0-100 123 MS83 8328 4164 25 40 31098 0-80 176 download: |

Hydraulic Motor,Radial Piston Hydraulic Motor,Hydraulic Orbital Motor,MS Series Hydraulic Motor,Axial piston hydraulic motor,Hydraulic Winch,Hoisting Winch,Free Fall Hydraulic Winch,Recovery Winch,Planetary Gearbox,300 Series Planetary Gearboxes,In-Line Planetary Gearbox,Right-Angle Planetary Gearbox,foot mounted planetary gearbox,400 Series Planetary Gear box,Final Drive,GFT Series Travel Drive,TGM Series Excavator Final Drive,Slew Drive,Wheel Drive,Winch Drive,Track Undercarriage,Steel Tracked Undercarriage,Rubber Tracked Undercarriage,Hydraulic Pump,

NINGBO BONNY HYDRAULICS TRANSMISSION CO.,LTD Add: No.36, the third road of Dagang, Beilun,Ningbo, Zhejiang, China Contact: Cathy Hsu (Sales Manager) Tel: +86-574-86879210 Fax: +86-574-86877981 E-mail:sales@bonnyhydraulic.com WebSite: http://www.bonnyhydraulic.com